## Slide 1: IP Phone(IP KTS) S/W Upgrade Guide for IPECS Unified (UCP, eMG800, eMG80)
EKR) R&D
Feb. 14, 2017

## Slide 2: Upgrade procedure
Upgrade should be done as below 2 steps.
First step is Kernel upgrade. And then goes to Application upgrade.
Connect to Unified System WEB Admin,
Choose S/W Upgrade
Boot upgrade of target Phone by using Unified system WEB Admin.
After completing Kernel upgrade,
the phone is reset automatically.
Application S/W upgrade by using Unified SYSTEM WEB Admin.
After completing Application upgrade,
the phone is reset automatically.
After completing Kernel upgrade,
goes to Application upgrade step

## Slide 3: Kernel upgrade -1
The file is in the PC.
Select folder and filename.
Kernel upgrade via Unified System WEB admin.
Kernel file name is GS98P12Ab-kernel_8xxx.rom
This status is changed to “Success” if upload is completed

## Slide 4: Kernel upgrade -2
Select the phone
and Press Upgrade button.
Press Upgrade Process, then, all stations are displayed that is related with uploaded file.
Select All, Press Upgrade button.
This status is changed to “Success” if upgrade is completed

## Slide 5: Application upgrade -1
The file is in the PC.
Select folder and filename.
Application upgrade via Unified System WEB admin.
Application file name is GS98P12Ab-app.rom
This status is changed to “Success” if upload is completed

## Slide 6: Application upgrade -2
Select the phone
and Press Upgrade button.
Upgrade Application of LIP-80xx phone
This status is changed to “Success” if upgrade is completed