## Slide 1: LIP-8000E / IP8800E Recovery Guide
R&D) Client Device Team
March 20, 2017

## Slide 2
Network Environment
Switch
Server (or PC)
IP : 192.168.10.100
NM : 255.255.255.0
GW : 192.168.10.254
LIP-8008E
IP8815E
LIP-8002E
IP8802
LIP-8012E
IP8820E
LIP-8024E
IP8830E
LIP-8040E
IP8840E
TFTP Server

## Slide 3
Recovery Mode (BootC)
Extract the recovery S/W package to the root directory of the TFTP server
Connect the phone to Switch by LAN cable and then turn on the phone
Press and hold the Navi-UP and 2 button while the phone is booting
(LIP-8008E / IP8815E : Vol-UP and 2 button)
When “Enter Password” is displayed, input the password : 1234
Enter the IP address, Subnetmask, Default Gateway, and TFTP server address
Phone downloads and writes the recovery S/W image
Please wait until the upgrade is automatically complete
After completion of the upgrade, the phone will return to normal operation
BootC Started
Enter Password
****
IP address?
192.168.1.100
Back OK
Netmask?
255.255.255.0
Back OK
Default GW
192.168.1.254
Back OK
BootC : used to recover the locked-up phone

## Slide 4
Back-up

## Slide 5
S/W Upgrade Precautions
- Upgrade IP Phones during users do not use phone (e.g. at dawn)
- Don’t Power-Off during upgrade
- Turn off the S/W Upgrade option before power construction such as the replacement of UPS
- Limit the number of simultaneous upgrade phones to prevent from exceeding the server capacity and network overload
- Use the HTTP(S) or FTP as the transport protocol
- Use the official S/W package
- Enter the correct server address
Network overload and transmission error
Abnormal termination during upgrade