## Slide 1: Unified SW V5.0 Introduction
Feb, 2021
Ericsson-LG Enterprise

## Slide 2: Contents
Highlight
What’s new - summary
V5.0 major features
V4.1 major features
License update

## Slide 3: V5.0 highlight
Black items in Unified V4.1 Temp (available from Oct/2020)
Blue items in Unified V5.0 (To be available from Q2/2021)
Support enhanced versions of CCX, IP-ATD, IPCR, UCS
vUCP – Trial license, Single instance vUCP, Hybrid GR
Integration - MS Teams interworking and enhanced SMDR interface
Support 1048ilss/EHSA V4, 1080i, 1048idss
Support new UCP100/SLTM4/8/32
Enhanced features for usability, management, security, …
Enhanced Apps
UCS 6.2*
IP-ATD 2.7A
IPCR 3.2
Integration
Refreshed G/W &
Enhanced features
UCP100/ New SLTMs
User Experience
Management
Security
Vertical markets
NMS 2.1**
CCX 1.1B
Virtual UCP
Trial license
Single Instance*
Hybrid redundancy*
* Unified SW Phase 5
** iPECS NMS: EoS as of Dec/2020
Web API / SMDR
New terminals &
Accessories
1080i*
1048ilss
1048idss*
EHSA V4

## Slide 4: What’s new - Summary
 | Unified v3.0 | Unified v3.1 | Unified v3.5 | Unified v4.0 | Unified v4.1 | Unified v5.0
UCS | v6.0 User base license Enhanced UX - Multi-login, Call log, IM continuity iOS Callkit support (iOS 10~) Push service for iOS/Android mobile Automatic failover to stand-by system in Geo-redundancy / T-Net environment (UCS Premium clients) On-demand call recording on mobile without MCIM resource Customization tool upgrade Flexible button window control option with main UCS window Search by name for non-UCS users | v6.1 AES encryption for GDPR v6.1 UCS premium server v6.1 UCS clients (Windows, Mac, iOS, Android) | v6.1+ TLS 1.2 support for port 7878/8899 | V6.1+ UX enhance (only with system S/W upgrade: Unified 4.0) Missed Call log sync Call forward only when UCS is out of service | V6.1+ Mac client Catalina OS support (Jun/`20) Android mobile client Android 10 support (Jun/`20) | V6.2 UCS Premium server iOS regular push support* iOS mobile client Support iOS regular push for IM/ notification* Mobile network IPv6 support** Mac client VPN support** Android mobile client Mobile network IPv6 support**
*Available with Unified SW V5.
**Not related with System SW version. Android/iOS mobile client IPv6 is only for mobile network IPv6, not for system/UCS server.

## Slide 5: What’s new - Summary
 | Unified v3.0 | Unified v3.1 | Unified v3.5 | Unified v4.0 | Unified v4.1 | Unified v5.0
IP-Attendant | IP ATD/ATDH 2.4 Personal Group Support Call log sync | IP ATD/ ATDH 2.5 AES encryption for GDPR | IP ATD/ATDH 2.6A Call Control, Name sync, One-step LDAP Search, Search in monitoring window, Recall information V2.6B (May/2019) TAPI call control for IP ATD, GDPR option, Separate flexible button, LDAP (search base, more filed, call priority option) | V2.6C (Dec/2019) *1 Call Server Geo Redundancy support (Dec/2019) | V2.7A (Oct/2020) Group setting (up to 100 per group) to reduce traffic PMS event save as CSV format Caller Name Display on Queued Group Call Hiding Auth Code Change folder for Outlook Contact Sync Add Wake-Up Type (Sun~Fri) | 
*1 : Application features (not related with system SW).
These application software will be available as scheduled above.

## Slide 6: What’s new - Summary
 | Unified v3.0 | Unified v3.1 | Unified v3.5 | Unified v4.0 | Unified v4.1 | Unified v5.0
CCX |  |  |  | V1.0 (Oct/2019, Unified 3.5+) |  | 
CCX R+ |  |  |  |  | V1.1B | 
IPCR |  | IPCR 3.0 support | IPCR 3.0+ HA HTTPS Local language | V3.1 (Sep/2019, Unified 3.5+) One-file call recording Delete registered agent Failover support for Call server Geo redundancy | V3.2 (Oct/2020) AWS support Recording cancel while auto call recording mode | 
NMS |  |  |  |  | V2.1 eMG100 1000i LDP-9200 | 
3rd party Solution | New 3rd party PMS Interface*1 Account code / Authorization code in ACD Manager Protocol*2 |  | RESTful API*1 SMDR Clickcall | Web API*1 (Mar/2020) Call Control APIs Call Event APIs Flexible Page API SMDR print in JSON format via WebSocket ACD Manager Protocol print in JSON format via WebSocket | SMDR enhance SMDR - ICM missed call SMDR - Called/Connected Info SMDR - Group call information SMDR - Abandoned call info Web API enhance SMDR Web API - Call ID added | 
*1 Need license (Refer to the details in license update section in the documentation)

## Slide 7: What’s new - Summary
 | Unified v3.0 | Unified v3.1 | Unified v3.5 | Unified v4.0 | Unified v4.1 | Unified v5.0
New Terminals | LIP-9040C (IPKTS) – color phone Automatic failover to stand-by system in Geo-redundancy / T-Net environment (LIP-9000 F/W upgrade required) One touch manual profile switching (LIP-9000 F/W upgrade required) | Support AES encryption for LIP-9000/9071 |  | Support new iPECS IP Phone 1000i series 1010i/1020i/1030i/1040i/1050i 1024idss | 1048ilss EHSA V4 | 1080i 1048idss
Enhanced IP DECT/ DECT | DECT feature enhancement (UCP only) Remote monitoring of 480H/500H Idle roaming support between zone of WTIM24 and zone of WTIM4/8 | Support UCP-WTIM24 for eMG800 | Support new IP-DECT bases and handsets | Support essential system features System directory support Call Server failover support Hotel check-out text message notify Call Back Alarm message integration (direct integration needed between alarm server and IP-DECT) |  | 

## Slide 8: What’s new
 | Unified v3.0 | Unified v3.1 | Unified v3.5 | Unified v4.0 | Unified v4.1 | Unified v5.0
Platform | Virtual UCP (vUCP, vVOIM, vUVM) E1R2 for Thailand/Brazil/ Argentina/Chile/Mexico UCP gateways can be installed behind NAPT / Failover support |  | New virtual call server license Support Amazon AWS Support new virtual gateways vMCIM Support virtual gateways for on-premise UCP call servers | Support vVOIMT (virtual transcoding gateway) for vUCP Kernel & Package upgrade for security enhancement for vUCP Call Server and gateways: vUCP / vUVM / vVOIM / vMCIM / vVOIMT vUCP VM message change (64K  32K) | vUCP Support trial license | vUCP Single instance support (Call Server, built-in vVOIM/vUVM) Hybrid geo redundancy vMCIM V2 upgrade
Enhanced Voice mail | Allows multiple trials on password input error when voicemail retrieval. Upload user greeting (.wav) files via Web. | VM cascading option User greeting upload VM time mode synced to system time mode |  |  |  | 

## Slide 9: What’s new - Summary
 | Unified v3.0 | Unified v3.1 | Unified v3.5 | Unified v4.0 | Unified v4.1 | Unified v5.0
Enhanced System features (1/2) | Enhanced UX Speed dial, Directory, Message, Missed call/Call back indication Call log management Improved terminology Visual VM for LIP-9071 Enhanced alarm/emergency features Automatic alarm call with announcement play (Internal and external) Automatic triggering of external relay Automatic paging triggering with alarm input Email notification to up to 10 email addresses Extended caller name display Receiver’s name display for pickup call Forwarder’s name display for forwarded call VM to email – Name display for intercom call Visual VM - Name display for intercom call | Normal paging volume control on a user basis ACD log-in group information Conference room Multi language on 9040C Background image change for 9040C | Support dual IP address for multihoming Enhanced emergency paging Phone lock / unlock Personal CCR for ICM call Differential Ring for station group “Barge-in” support during system call recording to VM (Need MCIM channels) “Barge- in” support when IPCR recording (Need MCIM channels) Improve MCIM channel management Networking support with UCP geographical redundancy case Support “auto idle” for Call log, TRANS, Speed, Menu, Dir, Msg Improve call log operation Call log support when Busy/DND/fwd to VM | UX enhance LIP-9000 LCD display - go back to default display page. UCS default ring tone change UCS missed call sync Easy and consistent alphabet input for name store and search Directory search: minimum 3 character  1 / 2 characters Internal call hold / retrieve by other’s DSS button Enhanced Call Routing Add a direct recall option to block a blind transfer to a busy extension. Support Personal CCR when announce-only mailbox option is enabled. Support more CCR options for BUSY/ERROR/NOANS destinations same as options 0-9. When “FWD IF OOS” for UCS client is set, forward incoming calls only when an UCS client is out of service. Add an option to provide MOH to caller while group call ringing | UX and Call management Programmable MOH by station Transfer using DIR search Flexible paging from MEX Transfer to a station in DND/FWD Idle on Hold for CC agent Block transferring a call Ringback tone for group Multi barge-in conference | 

## Slide 10: What’s new - Summary
 | Unified v3.0 | Unified v3.1 | Unified v3.5 | Unified v4.0 | Unified v4.1 | Unified v5.0
Enhanced System features (2/2) | Outbound PRI – Customized name presentation SMDR - Call info for incoming call to group EXEC/SEC with Call Forward – add new VM option Add an option to route calls to alternative destination when all ACD member is busy Add an option to route overflow calls to alternative destination when all members in ring group are busy and queue is overflowed. |  | Paging call log option Missed call log clear option Key pad tone on/off option CCR option for * and # Upload custom background color image for 9040C (Terminal feature) GCM  FCM | Hotel Features Create a wake-up group for wake-up call Hotel check-out text message notify (IP DECT) Headset button on/off option for guest room phone Room Status Change via a maid phone |  | 

## Slide 11: What’s new
 | Unified v3.0 | Unified v3.1 | Unified v3.5 | Unified v4.0 | Unified v4.1 | Unified v5.0
Enhanced Security | Access control option to Menu / PGM button Secure Hash Algorithm is changed from SHA1 to SHA2 Added default value for Station COS (for requesting countries) Added default value in allow/deny table as for white-list / black-list (for requesting countries) Leave change log for security related settings. | AES encryption for database (default off) AES encryption for voicemail recorded file (default off) | Strong user password for station web access and clickcall New license file support (encrypted by RSA2048) | UCS Premium - Separate UCS Web Admin Port and Data transfer protocol port for client. Add an option to show the station number instead of MEX mobile number to caller. Allow the SIP license registered for IPCR to be used only for IPCR. Standard SRTP for UCP Gateway using 256 encryption key Add an option for Remote Web Access Block for UCP Gateway | Web/Telnet enable/disable SMTP password digit increase DSS LED service for specific users | 
Management | Web admin enhancement for LDAP attributes Preset Flexible button is also supported for UC client | Trace route tool Web trace option More email alarm notification DECT phone monitor | Alarm notification support for geographical redundancy failover case | System Performance Status Display Packet capture for virtual gateways Web GUI to back-up voice mail greetings and messages (vUCP/eMG100) SIP Domain Name length (48  64) | Programming in excel style eMG800 time slot full alarm Decimal digit for mini-bar charge License for 3rd party coloring UCP100 SLIU disable option eMG800 ISDN clock sync | 
Software Assurance | Newly allowing system attendant to make an outgoing call in limited service mode. |  |  | Virtual UCP Only annual renewal with MNT1 .no multi year renewal  Removed MNT2~5 .Out of warranty below 5Y: doubled price .Out of warranty above 5Y: 100% of lic+MNT1 MNT1 step pricing by license portal (7 steps by port range) |  | 

## Slide 12: Unified V5.0 - major features

## Slide 13: vUCP enhance – Single Instance vUCP (1/2)
Adding single instance vUCP for cost reduction and simple deployment
  Single instance vUCP supports up to 600 system ports. (w/ built-in vVOIM/vUVM gateways)
  Expandable up to 2,400 system ports with external gateways. (w/o built-in vVOIM/vUVM gateways)
  Same vUCP licenses are commonly used for single instance/multi instances vUCP.
Single or multi instance installation (V5~)
Single Instance: up to 600 system port w/ built-in g/w
. Built-in vVOIM (default 6ch  up to 128ch
. Built-in vUVM (default 8ch  up to 64ch)
- Multi Instance: up to 2,400 system port w/o built-in g/w
(Unified V5.0)
Multi Instance installation (~V4.1)
System Port: up to 2,400port
External virtual gateways
vCore
vUCP CS
vVOIM
vUVM
vCore
vVOIM
vCore
vUVM
vCore
vVOIMT
vCore
vMCIM
vCore
vUCP CS
vCore
vUCP CS
vVOIM
vUVM
Disable
vCore
vVOIM
vCore
vUVM
vCore
vVOIMT
vCore
vMCIM
Up to 600ports
Up to 2,400ports

## Slide 14: vUCP enhance – Single Instance vUCP (2/2)
Installed vUCP (below 600ports) can migrate to single instance vUCP
Single instance vUCP can be expandable above 600ports
Multi virtual instances
(~ Unified SW V4.1)
Single / Multi virtual instances
(Unified SW V5.0~)
vUCP CS
50ports
6ch
8ch
50ports
6ch
8ch
248ch
2,400
ports
144ch
600ports
128ch
64ch
Below 600 system ports
Up to 600 system ports
Up to 128 vVOIM channels
Up to 64 vUVM channels
Add external virtual gateways
External
Virtual
Gateways
601~2,400 ports
Only with external gateways
vVOIM
vUVM
vUCP CS
vVOIM
vUVM
Multi instance vUCP
Single Instance
vUCP CS
50ports
6ch
8ch
248ch
2,400
ports
144ch
vVOIM
vUVM
Multi instance vUCP
Below 600ports
Reinstallation
DB adjustment
License transfer required*
Above 600ports
Disable built-in vVOIM/vUVM
DB adjustment
* License transfer is required with new vUCP S/N from re-installation.
(Unified V5.0)

## Slide 15: vUCP enhance – Hybrid Geo-Redundancy
Enhancing flexible and reliable deployment options by supporting Hybrid Geo-Redundancy
  Installed UCP600/2400 can be re-used as stand-by server (UCP licenses can’t be re-used to vUCP.)
vCore
vUCP CS
Stand-by
vCore
vUCP CS
Active
UCP600/2400
Stand-by
vCore
vUCP CS
Active
vUCP Geo-Redundancy
(Unified SW V4~)
Hybrid Geo-Redundancy
(Unified SW V5~)
Built-in vVOIM/vUVM can be used only with UCP600 (below 600ports)
Built-in GW can’t be used for UCP600/2400
UCP600/2400 SW needs to be upgraded to V5.0 as well.
(Unified V5.0)

## Slide 16: 1000i support
Supporting 1080i, expansion modules and accessories
1048ilss
1024idss
EHSA V4
1010i (2.4”)
1020i (2.8”)
1030i (2.8”)
1040i (3.5”)
1050i (4.3”)
1080i
Android 10 OS
7” Touch screen LCD
Built-in WiFi (802.3b/g/n/ac)
Built-in BT (BT 5.0)
8M pixel camera for video
HDMI, USB, Analog headset port
Simple foot stand
1048idss
48button paper DSS
Up to 4 ea per phone
1020i/30i/40i/50i/80i IPKTS
Unified V4.1
(Oct/2020)
Color LCD DSS
24 button x 2 pages
Up to 3 ea per phone
1020i/30i/40i/50i/80i IPKTS
EHSA V3
Unified V4.0
Unified V5.0
(Unified V4.1/5.0)

## Slide 17: Enhanced applications
Support enhanced applications with enhanced UX, management and Security features
(Unified V4.1/5.0)
*Available with Unified SW V5
**End Q1/2021. Not related with System SW version. Android mobile client IPv6 is only for mobile network IPv6, not for system/UCS server.
*** EoS in Dec/2020
UCS 6.2 | IP Attendant 2.7A | CCX 1.1B | IPCR 3.2 | NMS***
UCS Premium server iOS regular push support* iOS mobile client Support iOS regular push support for IM/notification)* Mobile network IPv6 support** Mac client Catalina OS support (Jun/`20) VPN support** Android mobile client Android 10 support (Jun/`20) Mobile network IPv6 support** | Feature enhancement Group based monitoring (up to 100 ext.) to reduce traffic PMS event log save as CSV format Caller Name Display on Queued Group Call Change folder for Outlook Contact Sync Password hide | Integration support for CCX Report+ | Integration support for IPCR on AWS Feature support Recording cancel while auto call recording mode | Support new system/ devices eMG100 1000i LDP-9200
Notes: Continue to support and enhance mandatory features like UX, management, security, OS update, IT/network environment change.
UCS
  Supporting regular push in iOS. iOS client and premium, standard UCS servers updated.
  Mac client VPN is supported now.
  Some mobile network IPv6 only. iOS and Android to support.
IP Attendant 2.7 A
CCX Report Plus
IPCR V3.2 support AWS
NMS: EoS since browsers don’t support flash anymore

## Slide 18: Refreshed UCP100/SLTMs (1/2)
New UCP100, SLTM4/8/32 with new DuSLIC solution
  Specifications are the same
    Current Intel DuSLIC-xT2 (Discontinued)  New DuSLIC-xs2 (same as eMG100)
  Model names stay the same
UCP100
SLTM4
SLTM8
SLTM32
(Unified 5.0)

## Slide 19: Refreshed UCP100/SLTMs (2/2)
Compatibility
  New UCP100 HW compatible with Unified SW V5 or higher
  New SLTM4/8/32 HW can be used with old Unified SW
  New SLTM firmware can be used with old SLTMs
    Old SLTM firmware can’t be used with new SLTMs
 | Unified SW 4.1 or earlier | Unified SW 5.0 or later
Current UCP100 HW | Y | Y
New UCP100 HW | N | Y
Current SLTM4/8/32 HW | Y | Y
New SLTM4/8/32 HW | Y | Y
Current SLTMs + New SLTMs HW | Y | Y
 | Current SLTM F/W | New SLTM F/W
Current SLTM4/8/32 HW | Y | Y
New SLTM4/8/32 HW | N | Y
> Unified SW compatibility
> SLTM F/W compatibility
(Unified 5.0)

## Slide 20: Unified v4.1 - major features

## Slide 21: vUCP Trial Support (1/2)
Support free vUCP trial for 90 days – need vUCP trial license.
  Applicable features and applications: vUCP call server, all system features and applications to maximum capacity
  Exceptions
    vUCP: vVOIMT/vMCIM
    Applications: CCX (no trial license), CRM for UCS (Need separate trial license for CRM for UCS)
How to get the trial license (refer to “vUCP Trial license download process” for details)
  Partner to download the following base licenses from the license portal and submit to ELG license manager to get the “vUCP-TRIAL” license.
    Base licenses (*.DAT) to download: vUCP-CS2400S, vUCP-SPLD, vUCP-MNTD-TRIAL, vUCP-MNT1
    * MNTD-TRIAL as free trial license indicator to ELG Account Manger so not to be invoiced.
  ELG license manager to provide the “vUCP-TRIAL” license.
    * vUCP-TRIAL license is valid from the date that ELG license manager generates using base license from the partner.
Use commercial version
Install vUCP & generate S/N
Generate
base license file (*.DAT with vUCP-MNTD-TRIAL) for trial and send them to ELG license manager
ELG license manager to provide trial license (with vUCP-TRIAL)
Free trial by uploading the vUCP-TRIAL license
Download the real license
Trial license reset request to ELG
Upload to the vUCP
(Unified V4.1)

## Slide 22: vUCP Trial Support (2/2)
Migrate trial version to commercial version before expiration
  Partner to send the trial license reset request (using “reset form” attached) to ELG license manager before expiration
  ELG to reset the trial license.
  Then, Partner can download the commercial licenses using the same serial number.
    vUCP-CS2400S, vUCP-SPLD, vUCP-MNTD, vUCP-MNT1 + required system licenses and application licenses in use (or to use).
  * System goes to the limited mode if no valid commercial licenses after trial expiration.
  ** Trial valid period can be found in the system license overview page.
  *** System to send expiring notice email (one-time notice before 30days and daily notices from 7days before expiration to pre-registered email in system Web-admin)
(Unified V4.1)

## Slide 23: MS Teams Interworking
Interworking with MS Teams client through Call2Teams M/W
3rd Party
SIP Ext.
Teams clients
with Phone System license
PSTN/SIP
iPECS UCP/ vUCP/ eMG
ELG terminals
MS Teams Client as a SIP client of UCP/eMG through Call2Teams
  iPECS Phone & Teams Client pairing
  One number / Dual forking
  Basic and supplementary call features
    Internal/external call, Transfer, Hold, Forward, Mute, Conf, Park, Pick-up
    Occasionally, signaling delay from MS Teams may cause various operation delay or failure for supplementary services
    Teams can join as Conf member but Hold not working.
Required licenses
  UCP/eMG
    UCP/eMG-MSTC (MS Teams Connect license, per user) for UCP/eMG as the number of MS Teams users
    SPL license as the number of MS Teams users
  Call2Teams
    Call2Teams subscription (license) per Teams user
  MS Teams license from Microsoft
    Office 365 admin account
    Office 365 E1/E3 subscription + Phone System add-on or E5 subscription per Teams user
Call2Teams
M/W (SBC)
MS Cloud
(Unified V4.1)

## Slide 24: Enhanced features
Category | Feature | Description
Integration | SMDR - ICM missed call SMDR - Called/Connected Info SMDR - Group call information SMDR - Abandoned call info SMDR Web API - Call ID SIP Paging Device | Support ICM missed call info in SMDR with call duration. Support original dialed info in SMDR for group/pick-up call. Support group call info in SMDR with answered/unanswered. Support abandoned call info in SMDR for disconnected before answer or during CCR announcement Added Call ID in SDMR Web API for call tracking Support DTMF relay during page for 3rd party SIP paging device
UX and Call management | Programmable MOH by station Transfer using DIR search Flexible paging from MEX Transfer to a station in DND/FWD Idle on Hold for CC agent Block transferring a call Ringback tone for group Multi barge-in conference | Support multiple different MOH on flexible buttons so play different MOH to caller when hold/transfer. (Number of VSF MOH is increased to 30) Support a transfer using DIR search Mobile extension can also make a flexible paging from external to system. Support transfer a call to a station in DND/FWD state using “override code”. Add an option “Go to idle on hold” specially contact center agent. Add an option to block a transfer for CO/Internal call Add more ringback tone options for group Enable barge-in conference joined by multiple users up to 32(UCP) 13(eMG)
Security/ Privacy | Web/Telnet enable/disable SMTP password digit increase DSS LED service for specific users | Support enable/disable Web/Telnet connection of phones (1000i only) by system Increased the number of digit to 64 for SMTP password (system / station) Added DSS LED service option to disable for specific stations
Management | Programming in excel style eMG800 time slot full alarm Decimal digit for mini-bar charge License for 3rd party coloring UCP100 SLIU disable option eMG800 ISDN clock sync | Added for SMTP configuration table, LCR tables eMG800 time slot full notification Support decimal digit for mini-bar charge License for 3rd party coloring solution (only for Korea) Added UCP100 disable option to use 2 SPL ports for others Added clock sync for eMG800 slave cabinets
(Unified V4.1)

## Slide 25: License update

## Slide 26: License updates with Unified v4.1
vUCP-Trial license
MS Teams Connector license (MSTC) for each system
CCX Report +
New licenses in Unified 4.1
*1 Clickcall license: Common use for current Clickcall client & new Clickcall Web API (RESTful)
*2 API-SMDR: Common use of SMDR RESTful API and SMDR Web API
Single system software
(Unified SW)
eMG80
eMG800
UCP600
Virtual
Machine
SMB
Mid
vUCP
UCP100
UCP2400
On-premise
Virtual
Call Server
SWA licenses
eMG/UCP
MNTD
MNTD2/3/4/5/6
MNT1/2/3/4/5
MNTU1/2/3
System Port License (SPL)
IP Extension
IPEXT
(ELG
IP/SIP Phones)
3SIPEXT
(3rd party
SIP Phones)
G/W &
Accessory
CO/BRI/PRI
SLT/DKTU/
DECT
Voicemail
Conference
Cabinet
UCP100
10port
50port
UCP600
10port
50port
100port
200port
500port
UCP2400
10port
50port
100port
200port
500port
1,800port
vUCP
10port
50port
100port
200port
500port
2,200port
eMG800
10port
50port
100port
200port
vUCP
MNTD
vUCP-MNTD-TRIAL
vUCP-TRIAL
> For CS2400
MNTD2/3/4/5/6
MNT1/2/3/4/5
MNTU1/2/3
> For CS2400S
MNT1/2/3/4/5
Apps & Feature licenses
IPN / TNLS / TNLCM
GR(Geo redundancy)
MEX
Hotel / FIDELIO
3rd PMS I/F (50 Guest room base)
TAPI
3SIPC/3SIPS
MS Lync
MSTC (MS Teams Connector)
AMSI, AMP
API-SMDR*2
API-CTI
API-CTI-EXT
API-AMP
UCS User lic (Basic/Adv/Power)
UCS Premium Server license
Clickcall*1
IP Attendant Office / Hotel
IPCR
CCX / CCX R+
NMS
Embedded VM ch/memory Exp
UVM channel/memory Exp
vUVM channel license
vMCIM channel license
UCP VOIP Switching
vVOIM/vVOIMT channel license
VCIM-DSPCL32 (32ch DSP)
Hardware
Licenses
1,200
w/SPL&EXPM
UCP100
199
600
2,400
50
UCP600
100
UCP2400
600
w/SPL
w/SPL
w/SPL
On-premise
eMG800
600
200
w/SPL
eMG80
2,400
50
vUCP
w/SPL
vUCP-CS2400S (SWL)
vUCP-SPLD
Virtual

## Slide 27: Web API - Licenses
Web API Licenses for 3rd party applications
Web APIs | Unified 3.5 | Unified 4.0 |  | 
Click to Call | Click to Call |  |  | 
Call Event |  | Dialing Proceeding Alerting Ringing Connected Released ReleasedAsc Rerouted Rerouting Failed Held Hold | Retrieved Retrieving Transferred Transferring Conferenced Conferencing DoNotDisturb Forwarding Registered UnRegistered MWI | ACD Agent LogOn ACD Agent LogOff ACD Agent Ready ACD Agent Not Ready ACD Agent Work ACD Agent Busy ACD Group Queueing ACD Group Queued ConfGroup Member ConfGroup MuteOn ConfRoom Member ConfRoom Usage SetMuteOn Configuration changed
Presence Event |  | Presence Start Presence Stop | Presence Event | 
Call Control |  | Make Call Answer Call Clear Connection Reroute Call Hold Call Retrieve Call Consultation Call Transfer Call Single Step Transfer Generate DTMF Reconnect Call | Set Forwarding Get Forwarding Set DND Get DND PickUp Conference Call Call Reject BusyService Set Call Back Get Call Status Call Park Call UnPark | Get MWI Flexible Page ACD Agent LogOn ACD Agent LogOff ACD Agent Set State ACD Group Control Conf Group Call Start Conf Group Call Add Callee Conf Grou0p Call Set Mute On Get Conf Room State Conf Room Open/Close
SMDR | SMDR via HTTPS | SMDR in JSON format via Websocket |  | 
ACD Manager |  | ACD Manager Protocol in JSON format |  | 
API-SMDR (per system)
System-base license for SMDR Web API
API-AMP (per system)
System-base license for ACDM Web API
CLICKCALL license(per seat)
API-CTI (server)
Server license for Call Control and Event API
API-CTI-EXT (per seat)
Client license for Call Control
Support 3rd party CTI servers*. API-CTI server license per CTI server including Alarm server for flexible page API and Call event based server for Event API.
In addition, need to add client license (API-CTI-EXT) as the number of clients to use CTI clients for call control.
System base license
This license supports both current AMP and AMP Web API

## Slide 28: vUCP – License update
CS2400S
600 ports
Default: SPL 50, vUVM 8ch, vVOIM 6ch
Max SPL 600ports
vUVM 64ch
vVOM 128ch
Added vVOIMT in Unified V4
Single instance vUCP Call Server (w/ built-in vUVM/vVOIM) GW is added in Unified V5
  All licenses can be used for single instance/multi instance vUCP call server and gateways.
vUCP Call Server
w/ external gateways
vVOIM
Max 248 ch
8ch base
increment
vUVM
Max 144 ch
8ch base increment
(per Virtual Machine)
(per Virtual Machine)
CS2400S
Default
SPL 50ports
2,400 ports
vVOIMT *1
Max 32 ch
vMCIM *1
Max 64 ch
(per Virtual Machine)
(per Virtual Machine)
*1 Internet connection is required for online license verification periodically.
New in Unified 4.0
New in Unified 5.0
vUCP Call Server
w/ built-in vUVM/vVOIM Gateway
Max SPL 2,400ports with external gateways
Same vUCP call server software (V5) & licenses
If enable built-in vUVM/vVOIM, max system port is up to 600ports.
For more than 600 ports, disable built-in vUVM/vVOIM

## Slide 29: vUCP – License update
vUCP gateway licenses for vUCP and UCP
vUCP
vUVM
(150ch per vUVM)
vVOIM
(250ch per vVOIM)
vVOIMT *2
(32ch per vVOIMT)
vMCIM *2
(64ch per vMCIM)
vUCP-VOIPCL8
vUCP-VMCL8
vUCP-vVOIMT-CL32
vUCP-vMCIM-CL64
vUCP-vVOIM-CL8 *1
vUCP-vUVM-CL8 *1
*1 vUCP-VMCL8 and vUCP-VOIPCL8 re-named as vUCP-vUVM-CL8 and vUCP-vVOIM-CL8 respectively for naming consistency from Unified 3.5
*2 vVOIMT/vMCIM: using software DSP (64ch)  periodic on-line license validation check
- vVOIMT: 2 soft DSP channel per 1 VOIP channel
- vMCIM: 1 soft DSP channel per 1 audio conference channel
UCP
UCP-vVOIM-CL8
UCP-vUVM-CL8
New in Unified 4.0

## Slide 30: Embedded license
vUCP built-in GW is added in Unified V5
 | eMG80 v2.2 | eMG80 v3.0 | eMG800 v2.2 | eMG800 v3.0 | UCP100 V2.2 | UCP100 V3.0 | UCP600 v2.2 | UCP600 v3.0 | UCP2400 v2.2 | UCP2400 v3.0 | vUCP (CS2400) | vUCP (CS2400S) w/ built-in GWs | vUCP (CS2400S) w/o built-in GWs
Built-in VM (Default  Max) | 2ch  8ch*1 | 2ch  8ch*1 | 4ch  8ch*1 | 4ch  8ch*1 | 8ch | 8ch | 8ch | 8ch | - | - | - | 8ch  64 (w/ built-in vUVM G/W) | 8ch  150 (w/ external vUVM G/W)
Built-in DSP VOIP (Default  Max) | 2ch  8ch*1 | 2ch  8ch*1 | 4ch  8ch*1 | 4ch  8ch*1 | 4ch | 4ch | 6ch | 6ch | - | - | - |  | 
Built-in VOIP Switching-G.711 only (Default  Max) | - | - | - | - | 0  16ch | 0  16ch | 0  24ch | 0  24ch |  |  |  | 6ch  128 (w/ built-in vVOIM G/W) | 6ch  250 (w/ external vVOIM G/W)
Phontage (Default) | - | - | - | - | - | - | - | - | - | - | - | - | -
Communicator (Default) | - | - | - | - | - | - | - | - | - | - | - | - | -
UCS Desktop (Default) | 2copy | (2copy)*3 | 5copy | (5copy)*3 | 2copy | (2copy)*3 | 10copy | (10copy)*3 | 20copy | (20copy)*3 | - | - | -
UCS Mobile (Default) | 2copy | (2copy)*3 | 5copy | (5copy)*3 | 2copy | (2copy)*3 | 10copy | (10copy)*3 | 20copy | (20copy)*3 | - | - | -
UCS User license (Default) | - | 2copy*3 (advanced) | - | 5copy*3 (advanced) | - | 2copy*3 (advanced) | - | 10copy*3 (advanced) | - | 20copy*3 (advanced) | 10copy*3 (advanced) | 2copy (advanced) | 2copy (advanced)
Clickcall (Default) | 2copy | 2copy | 5copy | 5copy | 2copy | 2copy | 10copy | 10copy | 20copy | 20copy | 10copy | 2copy | 2copy
IPEXT (Default  Max) | 32 | 32 | 30  600 | 30  600 | 30  199 | 30  199 | 10  600 | 10  600 | 10  2,400 | 10  2,400 | 10  2,400 | 30  600 | 30  2,400
Temporary License Activation | 6 times (1st 60days, 2nd to 6th : 30days each) |  |  |  |  |  |  |  |  |  |  |  | 
*1 : Built-in VM/VOIP for eMG80/800 : Max 4ch/8ch or 8ch/4ch
*2 : Replaced with UCS Desktop/Mobile from v1.2
*3 : Only one type can be enabled by system admin.

## Slide 31: SWA Policy Overview
Product | Year 1 | Year 2 +
eMG800 eMG80 P2 eMG100 UCP100 UCP600 UCP2400 | Full Service(60days) - Major S/W Upgrade for 60days from 1st installation + Basic Service (365days) - Minor Software Upgrade Full Service is available by downloading MNTD (optional) till the end of default maintenance period. System controls default maintenance period and MNTD allows only full service during this period. | Optional SWA or On-demand software upgrade licenses MNTD2/3/4/5/6: Optional SWA at initial installation (only one-time use of any one of MNTDx licenses) MNTU1/2/3*1: On-demand software upgrade licenses after default maintenance or MNTDx/MNTx expiration MNT1/2/3/4/5*2: Renewal licenses before/after MNTDx
vUCP (CS2400) | Full Service - Minor/Major Software Upgrade Must download MNTD (free) within 60days of 1st installation since vUCP is software base product. MNTD controls default maintenance period. | 
vUCP*3 (CS2400S) | > Year 1 (default) + Year 2 (mandatory)  Until Q1/2020 Full Service - Minor/Major Software Upgrade Must download MNTD + MNT1 at initial installation .MNTD provides 26 months including one-year mandatory period. .MNT1 ~5 can be also downloadable for additional period. | 
vUCP*4 (CS2400S) | > Year 1 (default) + Year 2 (mandatory)  After Q1/2020 (Exact date to be announced before applicable around early Q1/2020) Full Service - Minor/Major Software Upgrade Must download MNTD + MNT1 at initial installation .MNTD provides 26 14 months including one-year mandatory period. .MNT1 provides 12 months. .MNT1 ~5 can be also downloadable for additional period. is only available for renewal. (only yearly renewal, not multi-year renewal for license simplification) | 
*1 : MNTUx must be downloaded after the expiration of previous SWA licenses including default maintenance since MNTUx validity starts from the issue date. MNTUx doesn’t add remaining days of previous SWA period.
*2 : However, MNTx adds the remaining days so no issue when to download.
*3 : vUCP-CS2400S is replacing the previous CS2400 from Unified 3.5 in Jan/2019.
*4 : Automatic SWA step pricing by port range from the license portal is supported from Q1/2020.
> Year 3+
Optional SWA licenses: MNT1/2/3/4/5
3 different prices for MNTx
Regular renewal within grace period
Renewal below 5 years after SWA expiration
Renewal above 5 years after SWA expiration
> Year 3+
Optional SWA licenses: MNT1/2/3/4/5
3 different prices for MNT1
Regular renewal within grace period
Renewal below 5 years after SWA expiration
Renewal above 5 years after SWA expiration

## Slide 32: vUCP SWA policy with vUCP-CS2400S
 | On-Premise UCP | vUCP-CS2400 (200p default) | vUCP-CS2400S (50port by default)
SWA policy | Optional (1 ~ 5 years) Renewal optional (1 ~ 5 years) | Optional Renewal optional (1 ~ 5 years) | One-year mandatory Renewal optional (1 ~ 5 years) (yearly renewal with MNT1) - Regular yearly renewal before expiration: same price - Below 5 years after expiration: MNT1 at doubled price (standard MNT1 x 2) - Above 5 years after expiration: 100% of product price(all licenses) + standard MNT1
Pricing | Fixed pricing for each system - UCP100 / 600 / 2400 Multi-year discount | Fixed pricing for all ranges Multi-year discount | Step price for each range (7 steps) - 50 / 51~100 / 101~300 / 301~600 / 601~1,000 / 1,001~1,500 / 1,501~ No multi-year discount
 | 1Y | 2Y | 3Y | 4Y | 5Y | 6Y | 7Y | 8Y | 9Y | 10Y
Before expiration - regular yearly renewals
Below 5 years after expiration
In warranty
1 year
(mandatory)
MNT1 at doubled price
MNT1 at the price of
100% of product price including MNT1
Above 5 years after expiration
at initial installation
3 options for renewal
Standard price

## Slide 33: New license file & S/W version compatibility
System S/W Ver. | Old license file (issued by the end of 2018) | New license file (issued from the beginning of 2019)
3.5.11 or lower | Y | Y* * New license file is not compatible with Unified 1.3.9 or lower. There are several cases as below and please take the proper action for each case. For details, refer to “iPECS Unified S/W v1.3.9 or earlier Upgrade Procedure” guide, available from the global partner site. If SW is v1.3.9 or earlier with valid SWA in previous license file format (before license file upload) If SW is v1.3.9 or earlier with SWA expired (before license file upload) If you've already uploaded new license file with valid SWA, System works in limited service mode and "ILLEGAL LICENSE FILE" is shown in Software Maintenance raw & Purchased column of System Overview menu. If you've already uploaded new license file with valid SWA, System is rebooted repeatedly
3.5.12 or higher | N** ** Basically Unified 3.5.12 blocks uploading old license file format (issued by the end of 2018) however, it allows existing old license file in flash memory which was already uploaded in the previous software version. | Y

## Slide 35: UCS license policy for upgrade case
Cases | Policy | Remark
Only System S/W upgrade | Continue to user UCS 5.5 with per device license (no action for UCS) | 
UCS upgrade 5.5  6.0 | Need system s/w upgrade to Unified v3.0 under valid SWA Case 1) Full 6.0 features – Need to migrate license via the license portal UCSDS  Basic user UCSDSV  Advanced user UCSDP  Basic user + Premium server UCSDPV  Advanced user + Premium server UCSM  Advanced user Case 2) Only partial 6.0 features – No need any action | 
New deployment UCS 6.0 | Only per user license | 
UCS 6.0  UCS 6.0 user license upgrade | Following cases available. Need to pay the price difference Basic  Advanced user Basic  Power user Advanced  Power user | 
Current UCS Users
(Before v5.5)
New UCS Users
(v6.0 or after)

## Slide 36: Trial / License Transition
Cases | On-Premise UCP/eMG | vUCP
Temp license activation (for trial) | 6 times 1st time: 60days, 2nd to 6th: 30days each | 6 times 1st time: 60days, 2nd to 6th: 30days each
License transition support (only to the same customer) | eMG/UCP H/W replacement: Yes Previous S/N blocking from the license portal Migration to new system : Support by the end of 2017. LIK to UCP MG to eMG800 | H/W Server Change / Re-installation: Yes Previous Software S/N blocking from the license portal Migration to new system : No UCP to vUCP

## Slide 37: Temporary license activation
Support “Temporary license activation” up to 6 times
  1st time : 60days, next 5 times : 30days each
  Activation by System Admin - no need to download temporary license from the license portal
  Show Pop-up notice when enabling “Temporary License Activation” about “license upload required before expiration, limited service mode without valid licenses after expiration and recommendation on database download”.
  Daily email notice from 7days before expiration to pre-registered email in Web-admin.
  And also, daily notice to system attendant phone from 7 days prior to expiration (Disabled by default)
1st time
(60days)
2nd time
(30days)
3rd time
(30days)
4th time
(30days)
5th time
(30days)
6th time
(30days)
If valid licenses at expiration  Normal operation
If license in-valid at expiration  Disable feature or go to “limited service mode”. Refer to below table.
Need valid licenses from this
 | eMG80/800/UCP/vUCP | CM
1) System feature license | Disable system feature | Disable system feature except TAPI, LNKGW, GR. *TAPI, LNKGW, GR  Go to “Limited Service Mode”
2) Seat/Copy base license | Disable the whole application or feature with in-valid license | Goes to “Limited Service Mode”
3) SPL/IPEXT/3SIPEXT | Goes to “Limited Service Mode” | Goes to “Limited Service Mode”
Support emergency installation as well as multiple application trials
Simple and Quick to implement via Web-Admin

## Slide 38: Cases for going to “Limited Service Mode”
Valid licenses should be uploaded before expiration for the following cases
Temporary license activation expiration for SME/LME products
- For SME, if SPL/IPEXT/3SIPEXT are invalid, system goes to limited service mode.
When other application / feature licenses are invalid, just disable them.
- For LME, if IPEXT/3SIPEXT and seat base licenses are invalid, system goes to limited service mode.
When feature licenses are invalid, just disable them.
Default maintenance license(MNTD) upload within 60days of initial installation for LME products
- For SME, MNTD is not mandatory to install. It’s necessary to download MNTD when major software
upgrade is necessary during default maintenance period or download any other licenses for the first time.
LCM system running as a survivable mode for SME/LME
- For SME, needs reconnection to CCM system within 60days
- For LME, needs reconnection to CCM system within 30days
Validity Check
Normal Operation
Limited Service Mode
(Blocking only normal outgoing calls)
No
Yes
Upload valid licenses
or
2) Delete temp license from the DB
* LCM/Slave system – reconnection to CCM/Master system
Stand-by system running as a redundancy mode for SME
- Needs reconnection to Master system within 60days
Illegal (Intentionally changed) license file upload for SME/LME
* When uploading the license file, system date should not be earlier (past) than license issued date.
Ex) Uploading Jan/2018 issued license to system date Dec/2017 is illegal

## Slide 39: Limited Service Mode
System goes to the “Limited service mode” when it reaches license invalidation.
  Internal calls, Incoming calls and emergency outgoing calls are supported
  Outgoing calls are only allowed from the system attendant (to be supported from Unified v3.0)
  Remote PPP Connection is supported
Remote PPP Connection
Emergency Calls
No Outgoing Calls
Internal calls
Incoming calls
System Attendant
Outgoing calls from system attendant only

## Slide 40: License portal enhancement for vUCP SWA from Feb 25, 2020

## Slide 41: License portal enhancement - overview
vUCP SWA policy stay unchanged. Only license portal is enhanced for simplified vUCP SWA pricing.
  One-year mandatory at initial installation - In-warranty MNTD (14m) + mandatory MNT1 (12m)
  Yearly base renewal - only MNT1 available. Downloadable from 90days prior to expire date for next download
  3 renewal pricing options based on the renewal timing - within grace period (expire date + 30days), within 5years after expire, above 5years after expire
  Step pricing - 7 steps (~50, 51~100, 101~ 300, 301~600, 601~1000, 1001~1500, 1501~2000)
  No pro-rata applied - Pricing step is calculated based on the total SPL ports at the time of license download
License Portal is enhanced to fully support the SWA policy together with fixed step pricing from the dynamic pricing. The updated license portal (vUCP module) is to be open on Feb 25th, 2020. No impact on other license portal operation.
Simply partners need to follow the updated process in the license portal.
  Refer to the details on following slides.

## Slide 42: License portal enhancement - vUCP SWA automatic fixed step pricing
Before
  Dynamic pricing was applied: base price + xx% of sum of total SPL prices downloaded.
After
  Fixed step pricing is to applied: apply the fixed price for each range depending on total system ports (default 50 + downloaded SPL ports).
  Now ready to apply 3 renewal pricing options.
System port range | Standard Step pricing | Renewal from 30days after expire date to 5years | Renewal above 5years after expire date
50 | Fixed pricing depending on total number of SPL ports (7 steps) | Standard MNT1 x 2 | All licenses and standard MNT1
51~100 |  |  | 
101~300 |  |  | 
301~600 |  |  | 
601~1,000 |  |  | 
1,001~1,500 |  |  | 
1,501~2,400 |  |  | 
Before
After
System port range | Standard pricing (Same for renewal)
50 | Base price
51 ~ 2,400 | Dynamic pricing depending on number of total SPL ports (Base price + xx% of total SPL prices)
* 50% of each step price is added to MNT1 if GR license is in use.

## Slide 43: License portal enhancement – updated flow/condition
vUCP-CS2400S (SWL)
vUCP-MNTD (14m+12m = 26 months)
vUCP-SPLD
Port and feature licenses (optional)
Generate/ Download license file
vUCP-CS2400S (SWL)
vUCP-MNTD (14 months)
vUCP-SPLD
vUCP-MNT1
(12 months)
Generate/ Download license file
Port and feature licenses (optional)
Before | After | Remark
MNTDx/MNTx can be ordered | Only MNT1 can be ordered | MNT1 : 1year maintenance lic. (variable amount)
License file can be generated/ downloaded without MNTDx/MNTx | MNT1 license must be ordered for generating/downloading license files | “download” button will not be displayed if MNT1 is not ordered
MNTDx/MNTx prices were independent of installed SPL quantities | MNT1 price will depend on installed SPL quantities (7 steps) | If any inquiries on MNT1 pricing, send them to account managers.
MNTDx/MNTx can be ordered at any time | MNT1 can be ordered only after “90days before expire date” (Except for 1st MNT1 order) | 1st MNT1 order must be made at initial license order.
No additional charges for ordering after expire date | MNT1 price will be doubled if ordered 30days after expire date | Different rule will be applied for ordering 5-years after expire date
No additional charges for ordering after expire date | Total price of all installed licenses will be added to MNT1 price if ordered 5years after expire date | 
Before
Feb 24, 2020
After
Feb 25, 2020
> Updated flow/conditions in license portal for vUCP